JTAG protocol
- “It's I2C for testing”
- Popular transport layer for boundary-scan, debugging, etc
- ...but not limited to this.

---
SPI
Daisy chaining:
Signalling:

---
JTAG: a reconfigurable daisy chain.
- One or more slave systems in the scan chain
  - TAPs (Test Access Ports)
- Each slave has multiple register options
  - Instruction register (fixed bit-length, but same for all ICs)
  - Data register (variable bit-length, based on instruction)
  - More versatile, better performance for complex systems

---
How? the TMS signal

---
Types of instructions
Mandatory:
- BYPASS (1-bit DR) ← standardized instruction code
- EXTEST (write access to device pins)
- SAMPLE/PRELOAD (read access to device pins)
  Other:
- IDCODE (32-bit DR)
  - Not mandatory, but often supported
  - DR value identifies the TAP
  - If supported, IDCODE data register is the default connected data register after reset (allows scan-chain discovery)
- Other instructions are TAP-specific – usually allow some kind of data access

---
Example: CC3200 SoC

---
Example: CC3200 SoC
- By default, only one TAP: TI's “ICEPICK” router.
  - Can be configured to add various SoC internal TAPs to the scan chain.
  - Generic documentation available, CC3200-specific configuration found in OpenOCD
- Only internal TAP explicitly specified in the public datasheet is that of the user ARM Cortex M4 core.
  - Presumably others for pin access, testing features, access to the Wi-Fi core, etc.
- Debugging TAP scan chain configuration for CC3200:
ICEPICK TAP
Cortex M4 TAP
x
x
x
x
1
1
1
1
1
1
IR (4-bit)
IR (6-bit)
...
x
x
x
x
x
x
x
x
x
DR (?-bit)
DR (1-bit in BYPASS)

---
Example: CC3200 SoC
Q: So once we have access to the ARM core's TAP, what do we do?
  - A: we need read a whole bunch of stuff first.
    - ARMv7-M Architecture Reference Manual
    - ARM Debug Interface v5 Specification
    - ARM Cortex M4 Technical Reference Manual

---
Example: CC3200 SoC
Cortex M4 TAP
(same in all ARMv7-M
family processors)
MEM-AP
(same in all ARMv7-M
family processors)
access to “AP's”
via an address-based
access protocol
Memory-mapped debug registers
(Cortex M4-specific)
access to memory
via a another address-
based access protocol
System memory access
(Cortex M4-specific)
(other AP's)